## Slide 1
Preprocessing steps done:
Single file check:
  Upload file kent0001.vhdr to EEGLAB
  Verb epoching for expected nouns sentences (S205) – [-1 0.5] sec
  Baseline correction [-1 -0.5] sec
  Sanity check - Channel data (scroll)
  Data cleansing – removing blinks using ICA maps
  Rejecting extreme values [-100 100] uV
  Plot ERP (rectangular array) – focus on Pz, Cz, CP1, CP2 electrodes

## Slide 2
Sanity check - Channel data (scroll)

## Slide 3
Data cleansing – removing blinks using ICA maps

## Slide 4
Plot ERP (rectangular array) – focus on Pz, Cz, CP1, CP2 electrodes

## Slide 5
Plot ERP (rectangular array) – focus on Pz, Cz, CP1, CP2 electrodes
Should Interpolate electrode?

## Slide 6
Next steps:
Run process on all data
Statistical analysis